## Slide 1: More Accurate Current Limiting
C. Brune
9/8/2025

## Slide 2
BMS Current Limit
Commanded Torque
Vdc/Motor Speed
Torque Limit
1 / (3 * P / 4 * flux_pm)
2D Look-up Table
Setting of torque limit doesn’t actually use a measured DC current value
DC Bus Voltage
Motor Speed
Torque Limit
Requested Torque
Commanded Torque
2D Look-up Table can be calibrated with actual maximum torque values given the battery requirements.
Existing
Proposed
The 2D table could be replaced by a control algorithm that uses the measured battery current if it is available.
Vehicle
Inverter
Vehicle
Inverter

## Slide 3: CMxxx BMS Current Limits
The CM200 does not have a DC current sensor.
DC Current is estimated from the motor current and motor voltage. Does not consider inverter efficiency.
Motor torque is estimated based on motor parameters and measured motor current.
BMS Current limit does not compare to the estimated DC Current, it just calculates a torque limit that assumes 100% efficient inverter.